## Slide 1: 2D VS 1D Convolution Layers For fast Keyword Spotting on Max78000

## Slide 2: Dataset: Multilingual Spoken Words Corpus
English subset
  31 Words:
    'right', 'forward', 'dog', 'bed', 'five', 'stop', 'off', 'down', 'house', 'zero', 'marvin', 'bird', 'wow', 'left', 'eight', 'visual', 'seven', 'yes', 'two', 'six', 'three', 'backward', 'tree', 'follow', 'four', 'happy', 'learn', 'one', 'nine', 'cat', 'sheila’
  Output labels:
    Left
    Right
    Non of both
Category | Number of Utterances
Training | 69869
Testing | 13118
https://mlcommons.org/en/
Notes: Wichtig Output!

## Slide 3: Feature Set: MFCC
Using Librosa library
  librosa.feature.melspectrogram
Audio sample of 16384 length
 128 x 64 Features per word
  128 windows
  64 fft bins

## Slide 4: State of the Art
[2]

## Slide 5: Hello Edge: Keyword Spotting on Microcontrollers [1]
Using Precomputed MFCCs
[1] https://arxiv.org/abs/1711.07128
[1]
[1]
Notes: According to this paper Depthwise seperable CNNs are best performing 2D convolutional networks
But Depthwise cnn are not supporded by the CNN accelerator of the MAXIM78000, only by the Maxim78002
So we concentrate on the normal CNN of this Paper

## Slide 6: KWS20 on MAX78000
On Arm Cortex
On NN Accelerator
Segmented Audio Data (a) and its transpose (b) used as Input of the KWS20nets [2]
Notes: For 1D convolution I have the paper by Analog Devices on Key word Spotting
There they are not using MFCC or Fourie Transform
They are using segmented audio data as an input for the CNN

## Slide 7: Keywords Spotting Using the MAX78000 [2]
Using only 1D Convolutions
Segments of audio as Channels
[2] https://www.analog.com/en/design-notes/keywords-spotting-using-the-max78000.html
Visualization of a 1D-Con on 2D Input
https://stackoverflow.com/questions/42883547/intuitive-understanding-of-1d
-2d-and-3d-convolutions-in-convolutional-neural-n/44628011#44628011
Confusion matrix of KWS20net-v3 on KWS20 [2]
Notes: There Model is achieving excellent performance by using only 1D convolution layers

## Slide 8: Model Starting Point
2D Convolutional Network [1]
1D Convolutional Network [2]
Multilayer CNN
Using 2D Convolution
Accuracy in Paper: 92%
Approved Network for KWS
Depthwise separable networks not supported on Max78000 (only on Max78002)
KWS20netv2
CNN with only 1D Convolutions
Accuracy in Paper: 87%
1D conv are faster then 2D conv
Notes: As a starting point, I took the CNN for 2D convolution which is proven to be good at Key word spotting
And for 1D convolutions I took the KWS20net version 2
1D convolutions should be faster due to less calculations per layer,
but the accuracy of 2D networks could be better

## Slide 9: Optimizing CNN Model for Maxim78000

## Slide 10: MAXIM 78000 Neuronal Network Accelerator constrains
Max Linear Layer input: 1024
RAM 2*32.8KB 1
  Max Input-offset
    x8000
  Max Output-offset
    x8000
Max weights 432KB
1x1, 3x1, 3x3 Kernels
The architecture of the MAX78000 [2]
1 Self experienced value, due to lack of documentation of the synthesis step
Notes: Maxim comes with Arm cortex and a risk v microcontroller with its own Flash and Ram
The interesting part of the Maxim is the CNN accelerator which brings it own constrains for CNNs running on it
--name them
The cnn accelerator has its own ram but as I found out the max output-offset is limited to x8000
So that mean the maximum output size of a Layer which gets stored in the ram is 32.8KB

## Slide 11: Reducing model size
Network Size (Layers, Width) | Acc (Top1) 2 | Flash Max 432KB | RAM 1 Max 32.8KB
CNN 6 64 | 92% | 135kB | 125KB
CNN 6 32 | 89% | 71kB | 62.4KB
CNN 5 64 | 87% | 98kB | 125KB
Tab 1: Comparison of the CNN model with different numbers of layers and or max number of channels. No model has been post-quantized. The max Flash and RAM values refer to the Maxim78000.
1 Size of the largest layer output, used RAM between layers is roughly 2 as large (in and output)
2 Accuracy on differentiating all 31 words
Notes: So My first step after implementing the CNN of the Paper into pytorch using the AI8x library by Analog Devices
Was to reduce the Ram usage of the network so it can run on the Maxim
I found out that I have to reduce the width (number of channels) of the network and
I also have to use larger pool sizes of the Maxpool layers

## Slide 12: Optimized CNN
Combining Layer and Width
Layer reduction to 5
  Reducing #Ops
Reducing channels and increasing Maxpool size
  Reducing used RAM to 31.3KB
    Largest layer output: 16 x 63 x 31
  Limiting linear layer input to 966
Input 1x128x64
Output 3x1
Notes: I reduced the channel sizes of the first fiew layers and increased the number of Maxpools of the cnn from the paper
So it can fit on the Maxim

## Slide 13: Variations of the optimized CNN
 | Linear Layer size | Max Channels | Flash [KB] | RAM [KB]1 | Ops [M] | Inference time [us]
CNN for max | 966 | 64 | 53 | 31.3 | 5 | 1333
CNN smaller | 504 | 64 | 39 | 31.3 | 4.7 | 1328
CNN 32 | 504 | 32 | 14 | 15.65 | 1.4 | 814
Tab 2: Different Sizes of the optimized CNN in comparison. All networks are pre and post quantized
1 Size of the largest layer output, used RAM between layers is roughly 2 as large (in and output)
Notes: Now I want to see how I can speed up the Network by reducing its size it even further
It is possible by again reducing the channel sizes

## Slide 14: CNN suffers under size reduction and a large pool of words
Linear s. / channels | Accuracy | TP rate | FP rate
966 / 64 | 86% | 0.881 | 0.160
506 / 64 | 84% | 0.779 | 0.085
506 / 32 | 78% | 0.701 | 0.157
Tab 3: CNN in different sizes used to differentiate left and right
Linear s. / channels | Accuracy | TP rate of "left" | TP rate of "right" | FP rate of "left" | FP rate of "right"
966 / 64 | 93% | 0.328 | 0.491 | 0.005 | 0.012
506 / 64 | 92% | 0.28 | 0.474 | 0.002 | 0.017
506 / 32 | 89% | 0.02 | 0.302 | 0 | 0.013
Tab 4: CNN in different sizes used to differentiate left and right and non of both
Notes: As I trained the network on the dataset, I saw that…

## Slide 15: Using KWS20net on MLCommos

## Slide 16: KWS20net v2
Using it on MFCCs
  No good results for time-domain of ML Commos
Input 128 x 64
Output 1 x 3
Notes: The KWS20net version 2 looks like this…
We have 8 layers of 1d convolutions
I am using the network on MFCCs instead of directly on the time-domain because my results on that are unusable

## Slide 17: Kws20nets on Time-domain
Network | ai8xkws20 | ai8xkws20v2 | ai8xkws20v3
Accuracy (Top 1) | 20% | 15% | 13%
Quanticed Accuracy | 10% | 7% | 4%
Tab 4: Spotting 31 different words => pure guessing has accuracy of 3.2%
KWS20netv2 on predicting "left" or "right" gets only an accuracy of 58%

## Slide 18: Varieties of KWS20net-v2
 | Layers / Channels | Flash | RAM 1 | Ops | Inference time
KWS20net v2 | 8 / 192 | 360KB | 8.2KB | 5.9M | 929us
smaller | 6 / 160 | 155KB | 8.2KB | 3.2M | 601us
less Depth | 4 / 160 | 152KB | 8.2KB | 2.3M | 285us
less Width | 6 / 80 | 46KB | 8.2KB | 1.0M | 259us
Tab 5: Different Sizes of the KWS20net v2 in comparison. All networks are pre and post quantized
1 Size of the largest layer output, used RAM between layers is roughly 2 as large (in and output)
Notes: To compare to the CNN, I also did size reduction to this network to speed it up
_______________Zeig was man sieht _________________

## Slide 19: Accuracy of KWS20net does not suffer that much under size reduction
layer / channels | Accuracy | TP rate | FP rate
8 / 192 | 82% | 0.794 | 0.152
6 / 160 | 81% | 0.779 | 0.166
4 / 160 | 81% | 0.784 | 0.156
6 / 80 | 78% | 0.728 | 0.214
Tab 6: KWS20net in different sizes used to differentiate left and right
layer / channels | Accuracy | TP rate of "left" | TP rate of "right" | FP rate of "left" | FP rate of "right"
8 / 192 | 92% | 0.538 | 0.439 | 0.014 | 0.02
6 / 160 | 92% | 0.501 | 0.429 | 0.014 | 0.016
4 / 160 | 92% | 0.467 | 0.423 | 0.012 | 0.017
6 / 80 | 91% | 0.329 | 0.284 | 0.012 | 0.012
Tab 7: KWS20net in different sizes used to differentiate left and right and non of both
Notes: But compared to the CNN the…

## Slide 20: Speeding up networks with less Operations or/and less Ram usage
Chart: Inference time [us]
| 929 | 601 | 285 | 259 | 1333 | 1328 | 814
RAM [KB] | 8.2 | 8.2 | 8.2 | 8.2 | 31.3 | 31.3 | 15.65
Ops [M] | 5.9 | 3.2 | 2.3 | 1 | 5 | 4.7 | 1.4

## Slide 21: CNN can not be made much faster
Chart: TP rate against Speed of KWS networks
| 929
KWS20net v2 | 0.538
KWS20net Smaller | 0.501
KWS20net with less Depth | 0.467
KWS20net with less Width | 0.329
CNN for max | 0.328
CNN 32 | 0.02
CNN smaller linear layer | 0.28
Notes: In comparison we see that the CNN cant be made much faster compared to the 1D convolutional network

## Slide 22: 1D Convolution is way more efficient
Chart: 
| CNN 32 | CNN smaller linear layer | CNN for max | KWS20net v2 | KWS20net Smaller | KWS20net with less Width | KWS20net with less Depth
Mean TPR per run-time | 0.19779 | 0.28389 | 0.3072 | 0.52583 | 0.77371 | 1.1834 | 1.5614
Notes: We can also from the Data that

## Slide 23: 2D Convolution do have better Performance per network size
Chart: 
| KWS20net v2 | KWS20net Smaller | KWS20net with less Depth | KWS20net with less Width | CNN for max | CNN smaller linear layer | CNN 32
Mean TP rate per network size | 0.0013569 | 0.003 | 0.0029276 | 0.006663 | 0.0077264 | 0.0096667 | 0.0115
Notes: But never the Less, 1D networks need more Flash memory for good results compared to the 2D networks as we can see in the Meas tp rate per network size

## Slide 24: Conclusion
2D convolutions
More Networks around
Less Flash Memory usage
1D convolutions
Faster with same accuracy
More efficient
Less Ram usage

## Slide 25
 | Layers / Channels | Flash [KB] | RAM [KB] 1 | Ops [M] | Inference time [us] | Ops/Cycle 2 | Accuracy | TP rate | FP rate | Accuracy | TP rate of "left" | TP rate of "right" | FP rate of "left" | FP rate of "right"
KWS20net v2 | 8 / 192 | 360 | 8.2 | 5.9 | 929 | 127.0 | 82% | 0.794 | 0.152 | 92% | 0.538 | 0.439 | 0.014 | 0.02
KWS20net Smaller | 6 / 160 | 155 | 8.2 | 3.2 | 601 | 106.5 | 81% | 0.779 | 0.166 | 92% | 0.501 | 0.429 | 0.014 | 0.016
KWS20net with less Depth | 4 / 160 | 152 | 8.2 | 2.3 | 285 | 161.4 | 81% | 0.784 | 0.156 | 92% | 0.467 | 0.423 | 0.012 | 0.017
KWS20net with less Width | 6 / 80 | 46 | 8.2 | 1 | 259 | 77.22 | 78% | 0.728 | 0.214 | 91% | 0.329 | 0.284 | 0.012 | 0.012
CNN for max | 4 / 64 | 53 | 31.3 | 5 | 1333 | 75.02 | 86% | 0.881 | 0.160 | 93% | 0.328 | 0.491 | 0.005 | 0.012
CNN smaller linear layer | 4 / 64 | 39 | 31.3 | 4.7 | 1328 | 70.78 | 84% | 0.779 | 0.085 | 92% | 0.28 | 0.474 | 0.002 | 0.017
CNN 32 | 4 / 32 | 14 | 15.65 | 1.4 | 814 | 34.40 | 78% | 0.701 | 0.157 | 89% | 0.02 | 0.302 | 0 | 0.013
1 Size of the largest layer output, used RAM between layers is roughly 2 as large (in and output)
2 To calculate the Operations per Cycle the maximal CNN accelerator frequency of 50MHZ is assumed

## Slide 26: Demonstration of the KWS20net with less Depth